## Slide 1
Liba Krejzlikova
Business Development & Marketing Manager
Use of JETT Plasma Lift Medical in DERMATOLOGY

## Slide 2
Use of JETT Plasma Lift Medical in DERMATOLOGY
JETT Plasma Lift Medical
ETT Plasma Lift Medical is a smart portable DC (direct current) electric plasma
str. 02/03

## Slide 3
Use of JETT Plasma Lift Medical in DERMATOLOGY
Plasma
Electric plasma is a ionized gas in the air (containing free electrons), created by high voltage about 5000 V, which is between the tip of the device and skin of a patient and maintaining distance of 1-2mm
str. 02/03

## Slide 4
Use of JETT Plasma Lift Medical in DERMATOLOGY
DC fulguration
The main effects are achieved with “a plasma discharge” generated by DC voltage
Plasma discharge generates heat & warms the skin
Generated sparks in AC fulguration (all competitors on the market) operate on a relatively big area about 3-5 mm2
Jett Plasma Lift Medical uses DC fulguration with the spark flow area of 0,1 mm2
str. 02/03

## Slide 5
Use of JETT Plasma Lift Medical in DERMATOLOGY
Direct current plasma technology
XXXX
str. 02/03

## Slide 6
Use of JETT Plasma Lift Medical in DERMATOLOGY
Direct current plasma technology
XXXX
str. 02/03

## Slide 7
Use of JETT Plasma Lift Medical in DERMATOLOGY
2 ways of JETT Plasma Lift Medical use
1. Contact treatment - silver applicators:
2. Contactless – golden applicator:
str. 02/03

## Slide 8
Use of JETT Plasma Lift Medical in DERMATOLOGY
2 ways of JETT Plasma Lift Medical use
Contact treatment - silver applicators:
- Tingling, no burning
- No anaesthesia is needed
- Intensities 1-5
Every cell has a membrane potential. Inner side has a negative charge, the outer side has a positive charge. As the skin is ageing, the electric charge is distributed alternatively along the membrane, and the electric voltage of the membrane is changed.
Plasma is able to get the membrane potential back to equilibrium.
str. 02/03

## Slide 9
Use of JETT Plasma Lift Medical in DERMATOLOGY
Silver applicators treatment
XXXX
str. 02/03

## Slide 10
Use of JETT Plasma Lift Medical in DERMATOLOGY
2 ways of JETT Plasma Lift Medical use
Contactless – golden applicator:
- heating, burning - resurfation
- anaesthesia needed
- Intensities 6-8
- effect of plasma flows on tissues:
str. 02/03
Scanning (continual movements) = superficial burn of the skin (like peeling)
Dot-by-dot (max 3 seconds at 1 place) = microtraumas in dermis, stimulates fibroblasts to produce collagen
Together: very effective peeling, tissue recovery, skin tightening, improvement of flexibility and stimulation of immunity and resistance of the tissues

## Slide 11
Use of JETT Plasma Lift Medical in DERMATOLOGY
Golden tip use
The highest intensities (6, 7 and 8) are able to destroy skin cells. The tip of the device can reach temperatures up to 80°C.
A relatively low electric power, at maximum 1.8 W is applied and as it affects only a small area, it is able to cause the evaporation of cell liquids.
High temperature causes coagulation of tissue and blood proteins, which is used for stopping a small bleeding – to closure of small veins (with a diameter of 2-3 mm.)
The discharge is applied with a smaller power (1.8 W), compared to common electrocauters
str. 02/03

## Slide 12
Use of JETT Plasma Lift Medical in DERMATOLOGY
Indications
angioma senilis
verrucae seborrhoicae
verrucae plane
angiokeratoma
teleangiectasis
lentigo
fibroma molle
keratoacanthoma
str. 02/03

## Slide 13
Use of JETT Plasma Lift Medical in DERMATOLOGY
Indications
condyloma accuminata
moluscum contagiosum
verrucae vulgares
verrucae filliformes
naevus capillaris
naevus arraneus
keratosis actinica
keratosis senilis
keratosis seborrhoica
str. 02/03

## Slide 14
Use of JETT Plasma Lift Medical in DERMATOLOGY
Types of treatment
Superficial and deep wrinkles
Small warts
Fibromas and hemangiomas
Couperosis (dilated vessels) – for closing vessels
Pigment spots
Scars
Bleeding/ capillary bleeding/ after a minor surgery/ stops bleeding
str. 02/03

## Slide 15
Use of JETT Plasma Lift Medical in DERMATOLOGY
Contraindications
Pacemaker, Holter blood pressure monitoring system or ECG
Other implanted electrical device
Epilepsy
Pregnancy
Metal implants in the treatment area
Skin problems, inflammation diseases - erysipelas
Oncological disease
Other non-controlled or hardly-controlled disease
str. 02/03

## Slide 16
Use of JETT Plasma Lift Medical in DERMATOLOGY
Case interpretation
50 years old patient
after surgical blepharoplasty 6-7 years ago
main problem: superficial and deep wrinkles around the eyes
str. 02/03

## Slide 17
Use of JETT Plasma Lift Medical in DERMATOLOGY
Protocol of treatment (EUROPE)
Informed consent
Contraindications
desinfection
local anaesthesia without vasoconstriction part like epinephrin etc.
treating upper and lower eye lid – scanning 5-7 min. to visible flush or erythema
str. 02/03
Before

## Slide 18
Use of JETT Plasma Lift Medical in DERMATOLOGY
Protocol of treatment
erythema means warming dermis and starts tissue recovery, its tightening, improvement of flexibility and it also stimulates immunity and resistance of the tissues
apply dot-by-dot only on upper eye lid – deeper damage of the skin
contraction of collagen
str. 02/03

## Slide 19
Use of JETT Plasma Lift Medical in DERMATOLOGY
After treatment
skin is disinfected by the doctor / therapist after the treatment.
Immediately after treatment apply one of healing creams (e.g. “cica” cream) which contain panthenol and hyaluronic acid and are suitable to be applied to injured and irritated skin and accelerate reparation of epidermis.
disinfect the treated area twice a day after washing for 7-10 days after the procedure and after that always apply healing cream. This procedure has to be repeated until the spontaneous separation of crusts.
corrective cosmetics can only be used after healing of the epidermis / if necessary, Oxygenetix cover breathable products can be used.
Patient has to avoid sunlight after surgery. If the skin is exposed to sun rays, it is necessary to apply sunscreen with SPF 50 +, have sunglasses and head cover.
It is advisable to visit the doctor / therapist after one and two weeks after the procedure.
str. 02/03

## Slide 20
Use of JETT Plasma Lift Medical in DERMATOLOGY
After treatment
2nd - 3rd day after: erythema, oedema, scab (crusts)
4th day after: small erythema, without oedema and separating or peeling scabs
5th - 8th day: area around the eyes without the scabs
without any different colours of treated area
patient can apply make-up
seeing rejuvenation skin, reduced wrinkles, skin tightening
str. 02/03

## Slide 21
Use of JETT Plasma Lift Medical in DERMATOLOGY
Recommendation
apply suncream SPF 50+
use sunglasses
about 2 months
the top results after 2-3 months
As an addition, you can use cosmetic treatment with Jett Plasma Lift Medical (silver applicators)
str. 02/03

## Slide 22
Use of JETT Plasma Lift Medical in DERMATOLOGY
JETT Serum Liftvital (30ml or 400ml)
After active healing period
    Cooling effect
Lifting effect
Better and faster regeneration
Neocollagenesis boost
Beauty procedure
Perfect to use with silver applicators
Lifting effect
Permanent daily use
Lifting effect
Extension of blepharoplasty effect & other anti-aging treatments
str. 02/03

## Slide 23
Use of JETT Plasma Lift Medical in DERMATOLOGY
After the treatment
str. 02/03

## Slide 24
Use of JETT Plasma Lift Medical in DERMATOLOGY
Pictures 4 days after
str. 02/03

## Slide 25
Use of JETT Plasma Lift Medical in DERMATOLOGY
Pictures 3 months after
str. 02/03

## Slide 26
Use of JETT Plasma Lift Medical in DERMATOLOGY
Before/After
str. 02/03

## Slide 27
Use of JETT Plasma Lift Medical in DERMATOLOGY
Conclusion
excellent results
absolutely safe (ophthalmologist examination
after treatment, eyes without any problems, any damage)
possibility treatment of delicate area of the eyes
patient‘s satisfaction
str. 02/03