## Slide 1
Treatment Procedure for Jett Plasma Lift

## Slide 2
Treatment Procedure for Jett Plasma Lift
str. xx/xx

## Slide 3
1. Jett Plasma Lift Installation
str. xx/xx
1. Plug in the blue grounding cable.
2. Plug in the supply cable.
3. Plug the grounding cable in moisted bracelet.
Or to the electrode.

## Slide 4
1. Jett Plasma Lift Installation
str. xx/xx
4. If an electrode is used:
Place the electrode as close to the treated area as possible.
5. Screw the chosen tip on.
6. Plug the device in a power supply

## Slide 5
2. Setting of the Device
str. xx/xx
1. If message TAPE appears on the display, the moisted bracelet (electrode) is not applied correctly.
2. This is how the display looks like if the bracelet (electrode) is applied correctly.
3. Swipe the number scale with your finger to adjust time.
4. Touch the left button to adjust the intensity of the treatment. Set the intesity with the number scale. If you touch the button again, the device starts working (orange light is on).

## Slide 6
Warning
str. xx/xx
1. If the orange light on the display is on, the device is already active.
2. As you work with the device, the transparent part may get heated.
3. Never touch the metal tip, if the device is active. You might get hurt.
4. Neither clients nor the operating staff are allowed to wear any accessories during the treatment.

## Slide 7
Treatment procedure
str. xx/xx
1. Clean and dry skin thoroughly
2 . If a serum is used (not obligatory), apply it on the skin and gently massage it into the skin.

## Slide 8
First stage – Treatment with flat tip
str. xx/xx
3. Apply an indifferent gel
4. Divide the face into 6 parts. Each part is treated with a flat tip for 5 minutes.

## Slide 9
Movements for the treatment with flat tip
str. xx/xx
During the treatment, the tip is put on the skin.

## Slide 10
Movements for the treatment with flat tip
str. xx/xx
The flat tip should be gently pressed against the skin. However, the client must be comfortable with the treatment.

## Slide 11
Movements for the treatment with flat tip
str. xx/xx
Do not get to the hair area with the tip. Hair might get burned.

## Slide 12
Second Phase-Treatment with 5 mm tip or with pointed tip
str. xx/xx
Do not press against the skin during the treatment. The touch with the tip is light and the client feels comfortable.
The treatment time with the pointed tip 5 mm tip should be 10-15 minutes for the whole face.

## Slide 13
Second Phase-Treatment with 5 mm tip or with pointed tip
str. xx/xx
Make the tiniest possible moves on the whole face.

## Slide 14
Third stage-Treatment with 3 mm tip or with pointed tip
str. xx/xx
The 3mm tip is used mainly to treat the area around eyes.
Do not press against the tip during the treatment

## Slide 15
Movements for the treatment of the area around eyes
str. xx/xx
Do not press against the skin during the treatment. The touch with the tip is light and the client feels comfortable.

## Slide 16
Fourth Stage-Treating deep wrinkles
str. xx/xx
The pointed tip is used to treat deep wrinkles.
Do not press against the skin during the treatment. The touch with the tip is light and the client feels comfortable.

## Slide 17
Movements for the treatment of deep wrinkles
str. xx/xx
Move back and forth along the wrinkle. Repeat three times in one wrinkle. Do not press against the pointed tip. The touch must be gentle.
A zig-zag move, as if we wanted to sew the wrinkle. Repeat maximally 3 times on one wrinkle. Do not press against the pointed tip. The touch must be gentle.

## Slide 18
The point must be always in a right angle to the treated spot.
str. xx/xx

## Slide 19
6.Frequency of Treatments
str. xx/xx
Basic treatment
6-10 sessions
1-2 times a week
Following treatments
4 sessions-once every 2 week.
4 sessions-once every 3 weeks
Once a month

## Slide 20
7.Treatment of Body
str. xx/xx
The treatment procedure is the same as for the face treatment.