## Slide 1
Jett Plasma Lift Medical
Notes: Good morning ladies and gentlemen,
At first I would like to introduce myself. My name is Jana and I am an industry representative of Compex
company from Czech republic.
You have seen live surgery- noninvasive blefaroplasty and fibromas removal performed by our doctor Macková and I thank her very much for excellent job. She has treated patients with Jett Plasma Lift Medical device.

## Slide 2
Jett Plasma Lift Medical
str. xx/xx
CE MEDICAL 1023
D/C plasma device
Portable
230V
1.8W
contactless
Notes: Jett Plasma Lift Medical has European CE certification for medical devices. The device uses direct current to create a plasma discharge. It works with voltage 200 Volts and the highest output is 1.8 Watts. One of the biggest advantages is a fact that treatment with Jett Plasma Lift Medical is contactless. Discharge is produced between a tip and patient´s body.

## Slide 3
Technical design
str. xx/xx
contactless 1mm tip
0,5cm distance
0,1mm spot
0,6 - 1,8 W
0,5 cm
Notes: Necessery distance for plasma creation is 0.5 centimetres and the discharge is visible. If you touch the skin or hold the device up, plasma discharge is not created.
In comparison to AC electrocauters, Jett Plasma Lift Medical works more precise and enables to treat really small areas – affected spot size is only 0.1 milimetres.
The range of intensity, which you can set on the device is from 0.6 Watts to 1.8 watts. So when you want to work at different intensity level, you just set it up at the device and still work with only one machine.

## Slide 4
Indications
str. xx/xx
Notes: Indications are for example removing of fibroma, hemangioma, pigmented spots or warts. Plasma discharge can also soften and smoothe scars, remove spider veins and wrinkles, especially in the face. Procedure called noninvasive blepharoplasty is able to remove wrinkles around eyes and to modify eye shape.

## Slide 5
Blepharoplasty
str. xx/xx
Notes: Comments

## Slide 6
Blepharoplasty principle
str. xx/xx
epidermis
dermis
Notes: I am going to explain the principle of noninvasive blepharoplasty on next slides. Here we can see skin layers epidermis and dermis.

## Slide 7
Blepharoplasty principle
str. xx/xx
Resurfation
Notes: First treatment technique, which doctor Macková has performed, was scanning.
It warms the epidermis and makes superficial burns. This process causes resurfation (regeneration) of epidermis.

## Slide 8
Blepharoplasty principle
str. xx/xx
Dotting
Notes: During the second technique, dot-by-dot, plasma discharge penetrates deeply into the dermis and causes microtraumas.

## Slide 9
Blepharoplasty principle
str. xx/xx
Healing
Notes: During the second technique, dot-by-dot, plasma discharge penetrates deeply into the dermis and causes microtraumas.

## Slide 10
After treatment care
str. xx/xx
Serums with panthenol, hyaluronic acid, Vitamin C, lactic acid, etc.
SPF50
Sunglasses
We reccomend for example CICAPLAST Baume B5 SPF50
Notes: For post treatment care our key doctors developed special serum Jett Plasma Liftvital with panthenol, hyaluronic acid, vitamin C and other substances. Jett serum Liftvital works not only as a post tratment care, but due to its characteristics when used daily, it prolongs the effect of blepharoplasty.

## Slide 11
Notes: Thank you for your attention and we would be very happy if you come to our stand (27) to see our products.